## Slide 2: Flip flop - memory

## Slide 3: Binary
Memory
Logic to select values from memory

## Slide 4: We have investigated data manipulation
Ripple adder

## Slide 5: How do we make something useful?
Input
Output
Instructions
Memory

## Slide 6: John von Neumann

## Slide 7
He made major contributions to a number of fields, including mathematics (foundations of mathematics, functional analysis, ergodic theory, representation theory, operator algebras, geometry, topology, and numerical analysis), physics (quantum mechanics, hydrodynamics, and quantum statistical mechanics), economics (game theory), computing (Von Neumann architecture, linear programming, self-replicating machines, stochastic computing), and statistics.

## Slide 9: What is the purpose of the cpu?
The CPU executes programs (made up of instructions) using the fetch-decode-execute cycle

## Slide 10: Fetch – decode – execute
The CPU fetches an instruction
The CPU decodes the instruction to determine what action is required
The CPU then executes that instruction
This cycle is repeated once every clock cycle, therefore the clock speed determines how fast the instructions are executed by the computer

## Slide 12
Arithmetic Logic Unit (ALU) - Carries out the arithmetic and
logical operations. Add, subtract, compare, multiply and divide.

## Slide 13
Control unit - Responsible for interpreting instructions in a
computer program and then sending control signals to the
components.

## Slide 14
Registers - Used to store single pieces of data or single
instructions immediately before or after processing.

## Slide 15
Main memory (RAM)
Stores instructions and data needed by the program (volatile).
This architecture in which the data and program are stored in
the memory is known as the Von Neumann architecture.

## Slide 17
modelling
Input number, store, load, output
inp
sta 99
lda 99
out

## Slide 19
INP
STA A
INP
STA B
LDA A
ADD B
OUT
HLT
A DAT
B DAT
Add two numbers
https://www.vivaxsolutions.com/web/lmc.aspx
((without labels))
INP
STA 99
INP
STA 98
LDA 99
ADD 98
OUT
HLT

## Slide 20
lda h
otc
lda e
otc
lda l
otc
lda l
otc
lda o
otc
hlt
space dat 32
h dat 72
e dat 101
l dat 108
o dat 111

## Slide 21: Little man computer
Create a document and fill it with:
Screen shots
Document little man computer
Document your code
Flow charts
Screen shot the code working
Input two numbers, add them, display result
Input two numbers, minus them, display result
Input two numbers, display the smallest
Input a number, count down to zero
Input two numbers and multiply them
Input a number, output the cube (n*n*n)
Output all odd numbers less than 100

## Slide 22: http://www.yorku.ca/sychen/research/LMC/